## Slide 1: Data Manipulation
Overview and Applications

## Slide 2: Agenda
Overview of LabVIEW data types
Manipulating LabVIEW data types
  Changing data types
  Byte level manipulation of data
  Bit level manipulation of data
Applications involving data manipulation
  Data encryption
  Instrument I/O

## Slide 3: LabVIEW Data Types: Numeric
Byte
Unsigned Byte
Word
Unsigned Word
Long
Unsigned Long
Single Precision
Double Precision
Extended Precision
8 bits
8 bits
16 bits
16 bits
32 bits
32 bits
8 bytes
Sun: 16 bytes
Windows/Linux: 10 bytes
Power Mac: Double/Double
4 bytes
Notes: <number>
<footer>
<header>
<date/time>
Page 7-25:
Introduce the numeric data types shown on the slide.
For the integer data types, each small box represents one bit in the integer.
For the floating point data types, each box represents one byte.
Describe the ranges of data and precision that can be stored for each numeric datatype:
  Integers (blue terminals) cannot have fractional values.
  If only three or four digits of precision are needed, SGL data is adequate.

## Slide 4: LabVIEW Data Types: Arrays
Stored as handles containing:
  Size of each dimension (in unsigned long integers, U32s)
  Data (size of elements varies but is consistent through array)
To align data correctly, a few bytes of padding may be added before the first element of data
Array is a continuous block of memory
1D array of SGLs
4D array of I16s

## Slide 5: LabVIEW Data Types: Others
Booleans: 8 bits
  All zeros = FALSE, nonzero = TRUE
Strings: 1D array of unsigned bytes
Array of Strings: array of U32 handles to string locations
Paths: handles containing path type and number of path components in U16s
  Byte 0,1:
    0 (abs), 1(rel), 3 (UNC)
  Byte 2,3
    # of path components

## Slide 6: LabVIEW Data Types: Clusters
Data stored according to cluster order
Scalar data stored directly in cluster
Arrays, strings, and paths stored as a handle to the memory location where the data is stored
Padding may need to be added, depending on OS
Example: cluster of SGL, EXT, and 1D array of U16s
Windows
Mac
Sun

## Slide 7: Flattened Data
Flat data takes up a continuous block of memory
  Scalar and array numerics are flat
  Strings are flat
  Arrays of strings are not flat
  Clusters may be flat (if simple numerics, for example)
During File I/O LabVIEW automatically flattens all data to ease storage to disk
Flatten/Unflatten to/from String functions perform the same operations in memory

## Slide 8: Flattened Data
Flattened data normalized to standard form for platform independence
  Numeric data in big endian form (MSB first)
    Windows apps may need to be little endian – swap bytes
  Sun format for extended precision numbers
Flattened form does not have data encoding
  When unflattening, data type needs to be known
  Type descriptor used to define data type
*demo

## Slide 9: Type Descriptors
Sequence of word integers that can describe any data type in LabVIEW.
<length> <type code>
  <length> I16 size in bytes (including length word)
  <type code> description of data
  Some additional info may follow type code
  Arrays and clusters structured (since there are other data types)
  Can quickly get complicated to decipher
*demo

## Slide 10: Changing LabVIEW Data Types
Typecast
  Change data type of information
  Works with flat data, 1D arrays of flat data, and strings
  Default type is string
Flatten/Unflatten to/from String
  Work with all data
  Behaves like LabVIEW internal flatten function
*demo

## Slide 11: Byte Level Data Manipulation
Split / Join numeric values into new data
Swap Bytes/Words to reorder existing data
Convert data to unsigned bytes/words/longwords to manipulate at the byte level
Convert data to strings to use string functions for manipulation
*demo

## Slide 12: Bit Level Manipulation
Rotate Left / Right with Carry to move bits and effect other values
Rotate to move bits within a value
Logical shift moves bits, putting 0s in their place
Turn data into unsigned bytes to use these functions easily
For custom bit manipulation turn data into Boolean arrays
*demos (2)

## Slide 13: Applications of Data Manipulation - Encryption
Standards exist for process (NIST, private corporation, etc)
  Scrambled data is called ciphertext, unscrambled data plaintext
  Data often encrypted using a key – usually a specific number of random bits and error checking bits
    Ex: 64 bit key: 56 data bits, 8 parity bits (one per byte of key data)
    Symmetric-key (Private Key): each user has access to the same key
      Pro: can be very fast
      Con: easier to compromise (one key to compromise)
    Public-key: each user has a public and private key
All sorts of algorithms exist to encrypt data (DES, IDEA, Blowfish, etc)
Web has a good source of intro pages
  http://www.anujseth.com/crypto/

## Slide 14: How to Encrypt Data?
Hook a 3rd party DLL (or ActiveX control) into LabVIEW using the Call Library Node (complexities, speed, usability, etc)
Grow your own
  Probably not as secure (but good enough?)
  Probably easier to implement/understand
  Some options:
    Simple bit shifting
    Key ciphering with your own algorithm (ex: passwords)
    Implementation of known algorithm in native G-code
*demos (3)

## Slide 15: Applications – Instrument I/O
Instruments (GPIB, ethernet, RS-232, etc) can often transfer data to a host PC in a variety of formats
  ASCII: easiest to read but largest byte transfer
  Binary: more difficult to use but much more compact
    Will probably need to typecast data after it is received
    My need to byte swap data
Use binary transfers for faster data transfers
When possible, pick the smallest data type for transfer

## Slide 16: Applications - Waveform Transfers
ASCII Waveforms
Binary Waveforms
  1-byte integers
  2-byte integers
Notes: Pages 10-42 to 10-44:
Most instruments return a waveform as either an ASCII string or a binary string. A binary transfer is faster and requires less memory than an ASCII string transfer.
ASCII Waveforms:
  With 1,024 points, each between 0 and 255, you need a maximum of 4 bytes per point, or 4,096 bytes, plus any header and trailer information.
  Use the Extract Numbers VI to convert to an array.
Binary waveforms encoded as 1-byte integers:
  Use the String to Byte Array function to convert to an array.
Binary waveforms encoded as 2-byte integers:
  The same waveform requires 2,048 bytes, plus header/ trailer information.
  Use the Typecast function to convert to an I16 array and then Swap Bytes. The LabVIEW Advanced course covers typecasting in more detail.

## Slide 17: Questions?