## Slide 1: Data Manipulation
Overview and Applications

## Slide 2: Agenda
Overview of LabVIEW data types
Manipulating LabVIEW data types
  Changing data types
  Byte level manipulation of data
  Bit level manipulation of data
Applications involving data manipulation
  Data encryption
  Instrument I/O

## Slide 3: LabVIEW Data Types: Numeric
Byte
Unsigned Byte
Word
Unsigned Word
Long
Unsigned Long
Single Precision
Double Precision
Extended Precision
8 bits
8 bits
16 bits
16 bits
32 bits
32 bits
8 bytes
Sun: 16 bytes
Windows/Linux: 10 bytes
Power Mac: Double/Double
4 bytes
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: LabVIEW Data Types: Arrays
Stored as handles containing:
  Size of each dimension (in unsigned long integers, U32s)
  Data (size of elements varies but is consistent through array)
To align data correctly, a few bytes of padding may be added before the first element of data
Array is a continuous block of memory
1D array of SGLs
4D array of I16s

## Slide 5: LabVIEW Data Types: Others
Booleans: 8 bits
  All zeros = FALSE, nonzero = TRUE
Strings: 1D array of unsigned bytes
Array of Strings: array of U32 handles to string locations
Paths: handles containing path type and number of path components in U16s
  Byte 0,1:
    0 (abs), 1(rel), 3 (UNC)
  Byte 2,3
    # of path components

## Slide 6: LabVIEW Data Types: Clusters
Data stored according to cluster order
Scalar data stored directly in cluster
Arrays, strings, and paths stored as a handle to the memory location where the data is stored
Padding may need to be added, depending on OS
Example: cluster of SGL, EXT, and 1D array of U16s
Windows
Mac
Sun

## Slide 7: Flattened Data
Flat data takes up a continuous block of memory
  Scalar and Array numerics are flat
  Strings are flat
  Arrays of strings are not flat
  Clusters may be flat (if simple numerics, for example)
During File I/O LabVIEW automatically flattens all data to ease storage to disk
Flatten/Unflatten to/from String functions perform the same operations in memory

## Slide 8: Flattened Data
Flattened data normalized to standard form for platform independence
  Numeric data in big endian form (MSB first)
    Windows apps may need little endian – swap bytes
  Sun format for extended precision numbers
Flattened form does not have data encoding
  When unflattening data type needs to be known
  Type descriptor used to define data type

## Slide 9: Type Descriptors
Sequence of word integers that can describe any data type in LabVIEW.
<length> <type code>
  <length> I16 size in bytes (including length word)
  <type code> description of data
  Some additional info may follow type code
  Arrays and clusters structured (since there are other data types)
  Can quickly get complicated to decipher

## Slide 10: Changing LabVIEW Data Types
Typecast
  Change data type of information
  Works with flat data, 1D arrays of flat data, and strings
  Default type is string
Flatten/Unflatten to/from String
  Work with all data
  Behaves like LabVIEW internal flatten function

## Slide 11: Byte Level Data Manipulation
Split / Join numeric values into new data
Swap Bytes/Words to reorder existing data
Convert data to unsigned bytes/words/longwords to manipulate at the byte level
Convert data to strings to use string functions for manipulation

## Slide 12: Bit Level Manipulation
Rotate Left / Right with Carry to move bits and effect other values
Rotate to move bits within a value
Logical shift moves bits, putting 0s in their place
Turn data into unsigned bytes to use these functions easily
For custom bit manipulation turn data into Boolean arrays

## Slide 13: Applications of Data Manipulation - Encryption
Encryption – make files or data transfers hard to read
  Standards exist for process (NIST, private corporation, etc)
    Scrambled data is called ciphertext, unscrambled data plaintext
    Data often encrypted using a key – usually a specific number of random bits and error checking bits
      Ex: 64 bit key: 56 data bits, 8 parity bits (one per byte of key data)
      Symmetric-key: each user has access to the same key
      Public-key: each user has a public and private key
  All sorts of algorithms exist to encrypt data (DES, IDEA, Blowfish, etc)
  Web has a good source of intro pages
    http://www.anujseth.com/crypto/

## Slide 14: How to Encrypt Data?
Hook a 3rd party DLL into LabVIEW using the Call Library Node (complexities, speed, usability, etc)
Grow your own
  Probably not as secure (but good enough?)
  Probably easier to implement/understand
  Some options:
    Simple bit shifting
    Key ciphering with your own algorithm (ie: passwords)
    Implementation of known algorithm in native G-code