## Slide 1: Introduction of Signal Integrity
Long Yang

## Slide 2: Contents
What is Signal Integrity
Why and When to Signal Integrity
How to Signal Integrity
    Fourier Transform
    Criteria of Non-Distortion
    Interconnect and Spectrum
    Noise
    Equalization
    Differential Signaling
Appendix
    RLGC Model
    Basic of Transmission Line
    S-parameter
    TDR

## Slide 3: What is Signal Integrity
Digital Signals
Transmission of signal is through interconnect
  Copper trace
  Waveguide
  Fiber
  Vacuum
  …
CPU
Memory
V
PI
SI
Modern High-speed is the trade-off result of all effective factors

## Slide 4: Why Signal Integrity
A measure of quality of an electrical signal
    Voltage
    Timing
Restore Signals from transceiver(TX) to receiver(RX) at RX side with acceptable tolerance.
    Without any distortion is impractical
    Analog property of digital signal
Why Distortion?

## Slide 5: Why Signal Integrity
Signal is transmitted as electrical activity
    Signal, power, EM wave, light…
    Signal/Power Integrity
    Electromagnetic Integrity
    Mechanical Integrity
    System Integrity
    …
Is signal happy and willing to go through the interconnects we designer?
    Listen to what signal is saying
    Democratic to signal
Impact from interconnect
    Cost, performance
    Silicon Chip Design VS Package/Board
  Why ustrip/stripline instead of waveguides are used to transmit digital signals?

## Slide 6: How Signal Integrity
Signal Noise Ratio
Bit Error Rate/Ratio
Eye Mask
Eye Diagram
Statistics

## Slide 7: Fourier Transform
  A mathematical operation that decomposes a signal into its constituent frequencies.
1st harmonic
1st harmonic +3th harmonic
1st harmonic +3th harmonic +5th harmonic +7th harmonic
+ 9th harmonic
How to form a Square wave
a square-wave is made up of a sum of odd harmonics
Why EMC cares about odd harmonics

## Slide 8: Criteria of Non-Distortion
Two ways to improve the quality of received signal
    Coding of transmitting signals x(t)
    Improving channel quality h(t)
h(t)
x(t)
y(t)
n(t)

## Slide 9: Criteria of Non-Distortion
Time Domain
    Constant magnitude
    Constant time delay
Frequency Domain
    Constant magnitude
    Linear phase difference

## Slide 10: Criteria of Non-Distortion
Why Low-Pass?
Amplitude Variation
Phase Variation

## Slide 11: Criteria of Non-Distortion

## Slide 12: Interconnect and Spectrum
Real digital signals strongly display analog behavior.
    Analog properties are easily treated in frequency domain
    Frequency-dependent interconnect property
Signal’s Spectrum
    Zero Rise Time -> Uniform Infinite Spectrum
    Limited Rise Time -> Decayed Infinite Spectrum
    Reasonable Truncated Spectrum -> fknee
antenna
Frequency
…
Transmission Line

## Slide 13: Interconnect and Spectrum
-T/2
T/2

## Slide 14: Interconnect and Spectrum
Knee Frequency fknee

## Slide 15: Noise
An unwanted perturbation to a wanted signal
    Random noise
    Deterministic noise
Mutual Capacitance
Mutual Inductance
Zs
Zo
Zo
Zo
Zs
Zo
Zo
Zo
ICm
Lm
near
far
near
far
ILm

## Slide 16: Equalization
Input signal
Low-pass signal channel
Received Signal
Sampling received signal
ISI: Inter-Symbol Interference.

## Slide 17: Equalization
ISI is given
How to mitigate ISI?
    ?
    ?
Why Pre-emphasis?
    Always effective?
    How to design?

## Slide 18: Single-ended VS Differential
  Two transmission lines are driven 180◦ out of phase (in the odd mode), and the differences between the voltages are used to recover the signal at the receiver using a differential amplifier.
    Power Saving
    Removal of Common-Mode Noise
    Virtual Reference Plane
    Double RX signal Level

## Slide 19
Q&A

## Slide 20: APP1: Return Path of Signal
An image current opposite of the signal current
Solid return path
Split/slot in return path
Notes: 由于异性电荷相吸,所以回路电流方向相反.这2个图都是示意图

## Slide 21: APP2: RLGC Model
Resistance/Conductance
    Related to geometry, length, cross-section, conductivity
    DC conductor loss
    AC Skin effect, frequency-dependent
Inductance
Capacitance
    Frequency-dependent
Skin Effect

## Slide 22: APP3: Time Domain VS Frequency Domain
Digital system is designed and correlated intensively in time domain
Correlation between TD and FD
frequency-domain
time-domain
change breakout
section characteristics
change PTH via
characteristics
mask violation!
resonance!

## Slide 23: APP4: Transmission Line
Basic Concept
  Used to model distributed signal path with the telegraph equation
  Important Parameters
    Characteristic impedance
    Propagation Constant
      Loss
      Phase/Time Delay

## Slide 24: APP4: Transmission Line
Property of Transmission Line
  Zc is frequency dependent in general
  Zc approximates to (L/C)^0.5 for low-loss case, and frequency-independent.
  Loss and phase variation cause signal delay and distortion.
Commonly-used transmission line
  Microstrip Line
  Stripline

## Slide 25: APP5: S-Parameter
Incident
Transmitted
S
12
S
22
Reflected
b
2
a
2
b
a
1
=
0
Z
0
Load
Reverse
1
Electrical Connection
Incident
Transmitted
S
21
S
11
Reflected
b
1
a
1
b
2
Z
0
Load
a
2
=
0
Electrical Connection
Forward
S
22
=
b
2
a
2
a
1
=
0
S
12
=
b
1
a
2
a
1
=
0
S
21
=
b
2
a
1
a
2
=
0
Insertion Loss
S
11
=
b
1
a
1
a
2
=
0
Return Loss
S
11
=
b
1
a
1
a
2
=
0
S
21
=
b
2
a
1
a
2
=
0
Insertion Loss
Return Loss

## Slide 26: APP6: Time Domain Reflectometry (TDR)
Measure a system of transmission lines in a digital system to ensure compliance with design guidelines
Understand the equivalent circuit of a component,
Simply verify that the simulations are predicting the transient response correctly.